## Slide 1: VMC Demonstration

## Slide 2: Overview
WHAT
  An explanation of VMC and how it affects multiengine flying
  Demonstration of the procedure used to regain control of the aircraft in the case it slows below the minimum controllable airspeed
WHY
  Safety!
  Without an understanding of VMC and the proper recovery techniques, decelerating below VMC can lead to a loss of control
CONTENT
One Engine Inoperative Airspeeds
VMC: Minimum Controllable Airspeed
VMC in the Airplane
VMC Demonstration
Hazards

## Slide 3: One Engine Inoperative Airspeeds
Safe Single Engine Speed
Minimum speed to intentionally render an engine inoperative
  Failing an engine below VSSE creates a high likelihood for loss of control & an accident
Not depicted on the airspeed indicator
  Used for training purposes
ACS
  Evaluator must not simulate engine failure until attaining at least 400’ AGL & VSSE (or VXSE or VYSE)
  Apply this during training
VSSE

## Slide 4: One Engine Inoperative Airspeeds
Best rate of climb speed with OEI
Blue line on the airspeed indicator
Used for max performance during OEI operations
  Or minimize descent, if above the single engine service ceiling
VYSE: Blue Line

## Slide 5: One Engine Inoperative Airspeeds
Min speed that the plane can be controlled when an engine suddenly becomes inoperative
Not a fixed speed
  Only fixed for the very specific set of circumstances under which it was tested during certification
  VMC varies with a variety of factors
VMC: RED Line

## Slide 6: VMC: Minimum Controllable Airspeed
The speed at which the rudder no longer has the authority to overcome the yaw caused by the critical engine being inoperative, under specific criteria mandated by the FAA
A lower VMC is good
VMC deals strictly with maintaining directional control, irrespective of climb performance
Published versus Actual VMC
  Published VMC is based on specific FAA mandated criteria
  Actual VMC varies based on the conditions, configuration, and technique
What is VMC?

## Slide 7: VMC: Minimum Controllable Airspeed
With an engine failed, the operating engine produces a yawing force toward the dead engine
  T x X
Rudder is used to counter the yaw and keep the plane straight
The rudder’s force is based on airspeed
  R x Y
  The slower the plane, the less airflow over the rudder, and therefore the less force
What Causes VMC?

## Slide 8: VMC: Minimum Controllable Airspeed
As an aircraft slows, and the rudder’s force decreases, the yawing force remains constant
Therefore, there is a speed where the rudder’s force = the yawing force
  T x X = R x Y
Slower than this speed, the aircraft yaws uncontrollably to the dead engine
  Rudder produces less force than the engine
What Causes VMC?

## Slide 9: VMC: Minimum Controllable Airspeed
The FAA sets forth criteria for manufacturers to follow when establishing VMC
  Critical Engine Inoperative
  Inoperative Engine Propeller Windmilling
  Maximum Available Takeoff Power
  Sea Level Conditions
  Most Adverse Legal Weight
  Most Adverse Legal CG
  Landing Gear Retracted
  Airborne & Out of Ground Effect
  Cowl Flaps in the Takeoff Position
  Maximum 5-degrees of Bank
  Flaps in the Takeoff Position
  Airplane Trimmed for Takeoff
How is VMC Certified?

## Slide 10: VMC: Minimum Controllable Airspeed
How Does Certification Criteria Affect VMC?
FACTOR | CONTROL | VMC
Critical Engine Inoperative | Decreases | Increases
Windmilling Propeller | Decreases | Increases
Max Takeoff Power | Decreases | Increases
Sea Level Conditions | Decreases | Increases
Most Adverse Legal Weight (Light) | Decreases | Increases
Most Adverse Legal CG (Aft) | Decreases | Increases
Gear Up | Decreases | Increases
Out of Ground Effect | Decreases | Increases
Cowl Flaps set for Takeoff (Open) | Increases | Decreases
Max of 5-degrees of Bank | Increases | Decreases
Flaps Set for Takeoff | Could go either way | Could go either way
Trimmed for Takeoff | Could go either way | Could go either way

## Slide 11: VMC in the Airplane
Control is lost when the moment of the thrust arm of the operating engine exceeds that of the rudder
Indication
  Full rudder is applied into the operating engine and the airplane continues to yaw toward the dead engine
  Visual reference point is the easiest way to recognize
Maintain a zero-sideslip to obtain an accurate VMC
Loss of Control

## Slide 12: VMC in the Airplane
Recovery
Recover the moment uncontrollable yaw or any stall symptom is recognized
Simultaneously reduce power & pitch
  Reduces the yawing moment
  Makes the rudder more effective
Recover to straight flight at VYSE

## Slide 13: VMC in the Airplane
VMC & Stall Speed
VMC decreases with altitude while stall speed remains the same
The altitude where VS = VMC and above is extremely dangerous
  A stall with one inoperative engine will likely enter a spin
  Departure from controlled flight can be sudden
  Twins are not required to demonstrate spin recovery

## Slide 14: VMC in the Airplane
Exceeding Critical AOA
recover at any symptom of an impending stall

## Slide 15: VMC Demonstration
Setup
Choose a visual reference point
Configuration
  Gear up, flaps & trim set for takeoff
  High rpm on both prop controls
  Cowl flaps open (as applicable)
Get stable about 10 knots above VSSE/VYSE

## Slide 16: VMC Demonstration
Setup
Power
  Left engine to idle power
  Right engine to takeoff power
Establish a zero sideslip
Brief the Maneuver
  “I will pitch up at a rate to realize a decrease of 1 knot per second. At the first indication of a loss of directional control or a stall, I will reduce power on the operating engine and lower the nose.”

## Slide 17: VMC Demonstration
Demo
Gently pitch up
Airspeed decreases and control effectiveness decays
  Increase rudder to counter yaw
  Increase aileron to maintain bank
Full rudder deflection = VMC
  Any slower results in a loss of directional control

## Slide 18: VMC Demonstration
Recovery
Reduce power on the operating engine and lower the nose
  Smooth inputs/adjustments
Reducing Power
  Reduce rudder to prevent yaw
  Maintain the reference point
Reestablish heading & VYSE
Return to normal flight
  Increase power on the idle engine
  Adjust rudder to maintain the reference point/heading

## Slide 19: Common Errors
Inadequate knowledge of the causes of loss of directional control at airspeeds less than VMC, factors affecting VMC, and safe recovery procedures
Improper entry procedures, including pitch attitude, bank attitude, and airspeed
Failure to recognize imminent loss of directional control
Failure to use proper recovery procedure
VMC Demo

## Slide 20: Hazards

## Slide 21: Hazards
Configuring the Airplane
In relation to VMC, configure as specified for the demonstration
  Understand the effects of different configurations on VMC & controllability
Real-Life Engine Failures
  Airplane will likely not be able to hold altitude OEI with excess drag
  Retract gear & flaps (and any other drag devices), & feather the propeller
  Reduced drag lowers the odds of reaching VMC or slower airspeeds

## Slide 22: Hazards
Distractions
They’re dangerous
  Remove them from view
  If a person, explain the situation & ask them to stop
Don’t fixate on the problem at the expense of flying the airplane
  Maintain airspeed & zero sideslip
Aviate, Navigate, Communicate
  Focus on flying, especially with an inoperative engine

## Slide 23: Hazards
SA & Disorientation
Maintain Situational Awareness & Orientation
  Starts with preflight planning – Know your options & have a plan
  Know where you are, what’s coming next, & stay ahead of the airplane
  If SA or orientation is lost, admit it, and fix it
Disoriented: Get the aircraft to a safe attitude, airspeed, and altitude
  Zero side-slip at VYSE, never below VMC
  Recover if below VMC
Ask for Help when it’s Needed
  ATC, Guard, other pilot/passengers, etc.

## Slide 24: Hazards
#1 Task: Safely flying the airplane
Divide attention between the aircraft, scanning, & communicating
  No responsibility should take full attention for more than a short period
  Verify aircraft performance often & consistently during any checklists
Understand what needs to be accomplished and when
  Use standard operating procedures & checklists
Recognize when you’re behind and find a way to catch up
  “Attack the closest alligator”
Task Prioritization

## Slide 25: Hazards
ACS Appendix 3 - XIII. Multiengine Operations
  Airplanes with normally aspirated engines will lose power as altitude increases because of the reduced density of the air entering the induction system of the engine. This loss of power will result in a VMC lower than the stall speed at higher altitudes. Therefore, recovery should be made at the first indication of loss of directional control, stall warning, or buffet.
  Do not perform this maneuver by increasing the pitch attitude to a high angle with both engines operating and then reducing power on the critical engine. This technique is hazardous and may result in loss of airplane control.
VMC & Density Altitude

## Slide 26: Questions?