## Slide 1: Airworthiness Requirements
General Overview

## Slide 2: Overview
WHAT
  Airworthiness requirements are the basis for deciding whether an aircraft is worthy of safe flight. They are what must be met to ensure an aircraft is safe and therefore legal to fly.
WHY
  For an airplane to be airworthy, specific documents must be on board and current, inspections must be completed, and instruments must be functioning, otherwise the airplane is un-airworthy, or illegal to fly.
CONTENT
Airworthiness
  Without an MEL
  With an MEL
  Required Inspections & Documents
  Airworthiness Certificates
Obtaining a Special Flight Permit
Record Keeping
Preventive Maintenance
Inoperative Equipment in Flight

## Slide 3: Inoperative Equipment Before Flight
Equipment requirements are designed for everyone’s safety
  Eliminates subjective safety decisions
The following procedures are minimum equipment requirements to be legal to fly
  Just because it’s legal, doesn’t mean it’s safe
  If you’re not comfortable, don’t fly
  Set personal equipment minimums
Methods for Determining Airworthiness
  Without an MEL (most common)
  With an MEL

## Slide 4: Airworthiness
Widely used due to simplicity and minimal paperwork
When inoperative equipment is found prior to flight, decide whether to:
  Cancel the flight, and have the equipment fixed, or
  Continue the flight by deferring inoperative equipment based on FAR 91.213(d)
FAR 91.213(d) – Verify the equipment is not required by any of the following:
  Day & Night VFR required instruments (FAR 91.205)
  Kinds of Equipment List and Equipment List
  Type Certificate
  Airworthiness Directive
If the equipment is not required, it must be
  Deactivated (or removed) and placarded as inoperative
  Any maintenance must be accomplished by certified maintenance personnel
Without an MEL

## Slide 5: Airworthiness
A
Night VFR: FLAPS
  Fuses (if required)
  Landing Light (electric)
  Anti-Collision Lights
  Position Lights
  Source of electricity for all equipment
FAR 91.205: Required Equipment for Day/Night VFR
Day VFR: TOMATO FFLAAMES
  Tachometer for each engine
  Oil pressure gauge for each engine
  Manifold pressure gauge (altitude engine)
  Airspeed Indicator
  Temperature gauge (liquid-cooled engine)
  Oil temperature gauge (air-cooled engine)
  Fuel gauge for each tank
  Flotation gear (for hire beyond glide distance)
  Landing gear position indicator
  Altimeter
  Anti-Collision Lights (certified after Mar 11, 1996)
  Magnetic Compass
  Emergency Locator Transmitter
  Safety Belts / Should Harnesses
Without an MEL

## Slide 6: Airworthiness
Kinds of Equipment List
Chapter 2 of the POH
Lists manufacturer required equipment based on type of flight
Equipment List
Usually found in the weight and balance data and/or POH
Specifies required equipment and equipment approved for installation in the aircraft
Without an MEL

## Slide 7: Airworthiness
Type Certificate
Formal description of the airplane, engine, propeller
Specifies the type of engine, propeller, number of seats, etc.
Lists limitations & information required for type certification
Cannot be changed without a supplemental type certificate
Found on the FAA TCDS website
Without an MEL

## Slide 8: Airworthiness
Airworthiness Directives (AD)
Notifies pilots of unsafe conditions and the required action
  Like a recall on a car
Two Categories:
  Emergency, requiring immediate compliance prior to further flight
  Less urgent nature requiring compliance in a specified time period
Not airworthy if an AD is not complied with by the designated date
  Must maintain record of compliance
Special Airworthiness Information Bulletin (SAIB)
  Info & guidance for safety issues that don’t meet AD criteria
  Tool to alert, educate, and make safety recommendations
Without an MEL

## Slide 9: Airworthiness
Without an MEL

## Slide 10: Airworthiness
MEL: Minimum Equipment List
  Precise listing of required equipment based on the type of flight
  Basically, combines 91.205, Kinds of Equipment List, ADs, & Type Certificate into 1 doc
  Common at airlines, but less common in general aviation
  Must be requested from the FAA
Required Equipment
  If equipment is inoperative, refer to the MEL to determine if it’s required
  If the equipment is not deferrable, it must be repaired prior to flight
  A special flight permit can be obtained if necessary to make repairs
With an MEL

## Slide 11: Airworthiness
Annual
  Aircraft less than 12,500 pounds flown for business or pleasure
  Requires an Airframe & Powerplant mechanic (A&P) with an Inspection Authorization (IA)
  May be substituted for a required 100-hour inspection
VOR: Must have been checked in the preceding 30 days (IFR requirement)
100 Hour
  Aircraft less than 12,500 pounds (except turbo powered) used for hire/flight instruction
  Requires an A&P at an FAA certified repair station, or done by the manufacturer
  Can exceed 100 hours by no more than 10 hours if enroute to inspection location
Altimeter/Pitot Static: FAR 91.411 – Requires inspection in the last 24 months (IFR)
Transponder: FAR 91.413 – Must be tested and inspected in the last 24 months
ELT: FAR 91.207(d) – If required, must be inspected every 12 calendar months
Required Inspections (av1ate)

## Slide 12: Airworthiness
Airworthiness Certificate
Registration Certificate
Radio Operator’s License
  If international
Operating Limitations (POH)
Weight and Balance
  Specific to the aircraft tail number
Required Documents (ARROW)

## Slide 13: Airworthiness
Standard Airworthiness Certificate
  White
  Normal, acrobatic, commuter or transport categories
  Remains in effect if the aircraft receives required maintenance & is registered in the US
Special Airworthiness Certificate
  Pink
  Primary, experimental, restricted, limited, provisional, and light-sport aircraft
  Limitations
    Generally, can’t be operated for hire & in some cases can’t carry passengers
    May be restricted to operations over sparsely populated areas or water
Airworthiness Certificates
Primary: FAR 91.325 | Experimental: FAR 91.319 | Restricted: FAR 91.313
Limited: FAR 91.315 | Provisional: FAR 91.317 | Light-Sport: FAR 91.327

## Slide 14: Special Flight Permit
FAR 21.197: Special Flight Permit
Authorization for an aircraft that is not currently airworthy, but is safe for a specific flight
  Flying to an airport where repairs or maintenance can be performed
  Delivering or exporting an aircraft
  Conducting customer demonstration flights
Obtaining a Special Flight Permit
  Contact the local FSDO or Designated Airworthiness Representative
  FAR 21.199: Must submit a statement to the FAA describing the flight

## Slide 15
Record Keeping (FAR 91.417)
Required inspections are in the aircraft and engine logbooks
100-Hour, Annual Inspection must be kept for 1 year or until the work is repeated
Records containing the following must be retained and transferred with the aircraft if sold:
  Total time in service (airframe, engine, propeller, rotor)
  Status of life-limited parts & Time since last required overhaul
  Current inspection status of the airplane
  Status of any ADs
  Copies of forms for major alternations

## Slide 16
Removing/Installing Equipment not on the Equipment List
  AMT must update the weight & balance for the new empty weight and CG, as well as the equipment list
Repairs and Alterations
  Major: Approved on Form 337 by a certified repair station, A&P with an IA, or a designated rep (14 CFR Part 43)
  Minor: Approved with an entry in the maintenance records by an A&P or certified repair station
Record Keeping (FAR 91.417)

## Slide 17
Who can perform Preventive Maintenance?
  FAR 43.3(g): Holder of a Part 61 pilot certificate
  Part 43 Appendix A(c)(30): At least a private pilot & registered owner
What is Preventive Maintenance?
  FAR 1.1: Simple or minor preservation operations & replacement of small standard parts not involving complex assembly operations
  Part 43 Appendix A(c)(30): Exhaustive list of authorized maintenance
  Be honest with your ability to perform the work satisfactorily & safely
Preventive Maintenance (AC 43-12)

## Slide 18
Performance Rules
  FAR 43.13: Basically, requires quality work and parts
Maintenance Records
  FAR 43.9(a): Any work done requires a logbook entry
    Description, completion date, signature, certificate #, kind of certificate
Return to Service
  FAR 43.7(f): At least a private pilot may approve a return to service
Preventive Maintenance (AC 43-12)

## Slide 19: Inoperative Equipment in Flight
Maintenance deferrals discussed here are not used for inflight discrepancies
POH procedures take precedence
Combine with risk assessment & mitigation techniques to assist in decision making

## Slide 20: Questions?